## Slide 1: OpenDaylight BGP Use-Cases
Giles Heron, Cisco
Notes: Credit to Ed Warnicke for some of these slides

## Slide 2: Agenda
Overview
Optimising Traffic using BGP-LS/PCE-P
Mitigating DDoS using BGP

## Slide 3: BGP/PCE-P Overview
Notes: Credit to Ed Warnicke for some of these slides

## Slide 4: BGP/PCEP Overview
OSPF
OSPF
BGP
Core
Edge
Route Reflector
Core
Edge
Route Reflector
Edge
Edge
BGP
Link-State, IPv4, IPv6 and Flowspec routes
MPLS LSPs via PCEP
Edge
BGP
PCE-P
OSPF
OSPF
PCE-P
OSPF
BGP
OSPF
BGP
OSPF
OSPF
OSPF
BGP
App
PCE-P
RESTCONF
BGP
Topology

## Slide 5: BGP Routes in ODL
LinkState: “Intra-Domain Routes”
  From ISIS or OSPF and learned via BGP-LS
  Used to create linkstate topology
Labeled Unicast: IPv4/IPv6: “Internet Routes”
  Can both learn routes and advertise them
Labeled Unicast: “Inter-Domain MPLS Routes”
  IPv4 routes with MPLS labels
FlowSpec: “Match/Action Routes”
  Like OpenFlow but using BGP - encoding actions as communites

## Slide 6: Routes – the BGP RIB (or RIBs!)

## Slide 7: Topologies
LinkState
IPv4
IPv6
PCE-P
BGP
RR
BGP
BGP
OSPF
OSPF
OSPF
OSPF
OSPF
OSPF
BGP-LS

## Slide 8: Use-Case: Optimising Traffic using BGP-LS and PCE-P
Notes: Credit to Ed Warnicke for some of these slides

## Slide 9: Using BGP-LS/PCE-P for Traffic Engineering
BGP-LS enables controller to see IGP topology
  Requires one BGP-LS speaking router per IGP area
PCE-P enables controller to set MPLS LSP paths
  Across one or many IGP areas
Stateful PCE-P enables global optimisation
Killer app for this is Segment Routing
  Bandwidth allocation tracked in the controller – not in the IGP
  Use PCE-P or NETCONF/YANG to configure LSPs at ingress

## Slide 10: BGP-LS Topology
Network: OSPF or IS-IS (IGP)
Routes: distributed from IGP into BGP-LS
RIB: Learned from BGP-LS speaker
Topology: Lists of nodes (routers) and links
RESTCONF URL:
http://localhost:8181/ restconf/operational/ network-topology:network-topology/topology/ example-linkstate-topology
OSPF
OSPF
OSPF
OSPF
OSPF
OSPF
BGP-LS
PCE
BGP-LS
Topo
Bldr
RESTCONF

## Slide 11: PCE-P Topology
List of all PCCs (Path Computation Clients)
For each PCC, list of LSPs for which it is the ingress LSR
Topology: Created by PCE-P plugin
  RESTCONF URL:
  http://localhost:8181/ restconf/operational/ network-topology:network-topology/
  topology/pcep-topology
MPLS
MPLS
MPLS
MPLS
MPLS
MPLS
BGP-LS
PCE-P
PCE-P
PCE-P
PCE
PCE-P
RESTCONF
Node LSPs
x ..,..,..
y ..,..,..
z ..,..,..
LSPs

## Slide 12: PCE-P LSPs (dynamic)
PCE creates MPLS-TE Label Switched Paths on PCC
Can modify LSP after setup or delete LSP
  RESTCONF URL:
http://localhost:8181/
restconf/operations/
network-topology-pcep:add-lsp
(update-lsp / remove-lsp)
MPLS
MPLS
MPLS
MPLS
MPLS
MPLS
BGP-LS
PCE-P
PCE-P
PCE-P
PCE
PCE-P
RESTCONF
Node LSPs
x ..,..,..
y ..,..,..
z ..,..,..
LSPs

## Slide 13: PCE-P LSPs (delegated)
PCC delegates locally configured MPLS-TE LSP to PCE for path selection:
Use update-lsp RPC to set path
interface tunnel-te1
ipv4 unnumbered Loopback0
signalled-name foo
!
destination 192.168.100.4
pce
delegation
MPLS
MPLS
MPLS
MPLS
MPLS
MPLS
BGP-LS
PCE-P
PCE-P
PCE-P
PCE
PCE-P
RESTCONF
Node LSPs
x ..,..,..
y ..,..,..
z ..,..,..
LSPs

## Slide 14: Demo: BGP-LS/PCE-P & SR
Notes: Credit to Ed Warnicke for some of these slides

## Slide 15: Use-Case: DDoS Mitigation
Notes: Credit to Ed Warnicke for some of these slides

## Slide 16: Advertising BGP Routes (Application RIB)
IPv4/IPv6 Routes: inter-domain routes
FlowSpec Routes: packet filters
APP RIB is config (main RIB is operational)
  APP RIB is a special-case peer of the main RIB
  (like iBGP but routes are sent to iBGP peers)
OSPF
OSPF
OSPF
OSPF
OSPF
BGP
OSPF
BGP
OSPF
App
BGP
RESTCONF
App RIB
BGP RIB

## Slide 17: Setting “Flows” (FlowSpec)
RFC5575 - Similar to OpenFlow but uses BGP to distribute match/action rules
Matches:
Source / Destination IP prefix
IP Protocol
Source / Destination TCP/UDP port
ICMP Type / Code
TCP Flags
Packet Length
DSCP Field
Fragment (DF, IsF, FF, LF)
Actions:
Rate limit
Traffic sampling
Redirection
Traffic marking (DSCP)
And more... (optional)

## Slide 18: DDoS Mitigation using uRPF and IPv4/IPv6
point 192.0.2.1/32 to null on all nodes
turn on uRPF
Advertise routes with next-hop of 192.0.2.1 to discard.
BGP
OSPF
App
BGP
RESTCONF
App RIB
BGP RIB
192.168.101.1/32
192.168.101.1/32 -> 192.0.2.1
192.168.103.1/32
192.0.2.1/32->null0

## Slide 19: Demo Advertising IPv4 Routes
Notes: Credit to Ed Warnicke for some of these slides

## Slide 20: Thank you